## Slide 1: Cislunar Explorers Lunar CubeSat: Instant Spacecraft, Just Add Water
Kyle Doyle Cornell University Department of Mechanical and Aerospace Engineering June 27th, 2019

## Slide 3: Spacecraft Operations

## Slide 5: Motivation
1. Flight resources such as propellant limit mission duration
  E.g. Cassini, Galileo, Dawn
2. Propulsion systems often costly, intricate, and hazardous
  Turbopumps, high-pressure vessels, cryogenic storage
  Hazardous materials e.g. hydrazine
  Cryogenic filling can be dangerous
  AMOS-6 incident:
    Accident during cryogenic propellant loading
    Payload hydrazine made the situation worse
3. CubeSats provide a low-cost approach to space exploration
There are additional limitations for nanosatellites
  Few high ∆V propulsion technologies available
  Strict mass, power, volume, and material constraints
  Secondary payload status can limit ground processing options
Images: NASA
Incident during AMOS-6 fueling for static fire.

## Slide 6: Water Electrolysis Propulsion Background
  Technology gap: High ∆V at the CubeSat scale
    CubeSat propulsion in its infancy
  CubeSat framework poses challenges
    Volume, mass, power constraints
    CubeSat restrictions preclude:
      High pressure vessels
      Cryogenic filling before launch
  Water has increasingly apparent abundance in the Solar System
    In-Situ Resource Utilization potential
  Water has uses beyond propulsion
    Human needs
    Radiation shielding
    Slosh damping
    Heat sink
Mueller, J., Hofer, R., and Ziemer, J. “Survey of Propulsion Technologies Applicable to CubeSats.” Jet Propulsion Laboratory, National Aeronautics and Space Administration: Pasadena, CA, 2010
Images: NASA

## Slide 7: Electrolysis Propulsion Background: Operation
Zeledon, R. A. and Peck, M. A. ”Electrolysis Propulsion for CubeSat-Scale Spacecraft,” AIAA SPACE 2011 Conference & Exposition, Long Beach, CA, 2011.
de Groot, Wim, et al. "Electrolysis propulsion for spacecraft applications." 33rd Joint Propulsion Conference and Exhibit. 1997.
McElroy, J. F. Electrochemical hydrogen separator system for zero-gravity water electrolysis. 4,950,371, August 21, 1990

## Slide 8: Water Electrolysis Propulsion Performance
Thruster test campaign in thermal vacuum chamber
  ~300 s specific impulse
  Similar to other electrolysis thrusters*
  Compare with cold gas (70 s) and LOX/LH2 (450 s)
Dense, green propellant storage
Simple operation with no actuated valves, low power
Subsystem synergy
  Thermal
  Attitude control
  Structures
ISRU potential
*James, Karsten, et al. "Hydros: High Performance Water-Electrolysis Propulsion for Cubesats and Microsats." Advances in the Astronautical Sciences Guidance, Navigation and Control 159 (2017): 2017-145.

## Slide 9: Interplanetary Optical Navigation
Adams, Van H., and Mason A. Peck. "Lost in Space and Time." AIAA Guidance, Navigation, and Control Conference. 2017.
Adams, Van H., and Mason A. Peck. "Interplanetary Optical Navigation." AIAA Guidance, Navigation, and Control Conference. 2016.

## Slide 10: Interplanetary Optical Navigation Performance
28,000 km 369,000 km
595,000 km 1,100,000 km
Inexpensive, robust, navigation in planetary systems
  Autonomous position and attitude determination from the same data
  Constant comms link for tracking not needed
Accuracy within tens of kilometers
  Mission simulation using rendered images from AGI STK
  Testing with real-world images from past missions and new photos
Original Images: NASA

## Slide 11: Impacts: Interplanetary Optical Navigation
Autonomous interplanetary navigation at CubeSat scale
No constant comms link for navigation/tracking
  Reduces spacecraft power consumption
  Reduces demands on ground segment
Applicable to other environments
  Gas giant moons systems
Hardware accessible for hobbyist and educators
  Raspberry Pi, multiplexer, 3 cameras: ~$200 total
Images courtesy of NASA

## Slide 12: Impacts: Water Electrolysis Propulsion
In-situ resource utilization potential
  Icy moon hoppers, small body sample returns
Water is abundant in the solar system
  Targets with water have scientific value
Could turn delta-v limits into delta-v increments
Image: NASA
Image: NASA
Image: ESA

## Slide 13: Questions?