## Slide 1
Lofted Environmental Venus Sensors (LEAVES)
Jeffrey Balcerski Ohio Aerospace Institute
Anthony Colozza (Vantage Partners, LLC), Gary Hunter (Glenn Research Center),
Maciej Zborowski (Vantage Partners, LLC), Darby Makel (Makel Engineering, Inc.)

## Slide 2: WHAT IS A “SWARM”?
“2a: a large number of animate or inanimate things massed together and usually in motion” – Merriam-Webster Dictionary
Order of magnitude lower in mass than a 1U cubesat (picosat or smaller)
Order of magnitude lower cost than SIMPLEX cost cap
At least ten individual units, having a common architecture and purpose, widely spatially distributed during an exploration campaign.

## Slide 3: PLANETARY SWARM PROBES
Swarms
Low cost
Many units
Widely distributed
Focused science
Some failure expected
High redundancy
Conventional
High cost
Single unit
Limited location/time
Comprehensive science suite
Zero fault/failure
High reliability
RESILIENCY

## Slide 4: PLANETARY SWARM PROBES
Swarms perform investigations that are either inappropriate or impossible for monolithic spacecraft.

## Slide 5: PLANETARY SWARM PROBES
KickSat (2015)
(1999)
Windbots (NIAC - 2017)
GOWON (2012)
Flexible Electronic Platforms / STANLE (NIAC – 2014)
Shapeshifters (NIAC - 2018)
Marsbees (NIAC - 2018)

## Slide 6: W H Y V E N U S?
Credit : ESA (Icarus, 2013)
Credit : ESA (Nature Geoscience, 2013)
Credit: JAXA (Nature Geoscience, 2017)

## Slide 7: V E N U S C H A L L E N G E S
Sulfuric acid clouds
Dense, extensive atmosphere
Highly reactive surface
Easy to arrive… Difficult to survive
Venus is a tremendous engineering challenge and a tantalizing science mystery
100 km: -112 C, 2.7x10-5 bar
68 km: -37 C, 0.07 bar
48 km: 93 C, 2.7 bar
0 km: 467 C, 93 bar

## Slide 8: APPROACH
Distributed, low cost, high resilience, low risk targeted science
Utilize electronic components for extreme environments (Venus)
Optimize for atmospheric investigations – low mass, high drag
“Passive” swarm – No active navigation, no swarm home/hive
Keep It Simple payload
  Single chemical species sensor
  Ambient temperature, pressure, accelerometer, gyroscope
  Transmit-only radio with radar wake-up trigger

## Slide 9: APPROACH
Short-lived Probes
Long-lived Platforms
VISE (2003)
Cupid’s Arrow (2014)
Venera (1982)
VAMP (2013)
HAVOC (2015)
Intermediate-Life Probe Swarms
Parallel data collection
Wide area coverage
Resiliency directly related to redundancy
But…
Redundancy is limited by scalability

## Slide 10: ENABLING TECHNOLOGY
2 cm
(NASA GRC / Makel Engineering Inc., 2016)
Highly sensitive MEMS chemical sensors
2-Stage Operational Amplifier IC
Conventional miniaturized electronics (-55° to 220° C)
24-Transistor Ring Oscillator IC
High Temp Electronics
  COTS power: Electrochem Solutions Inc. 200 MR Series (4410) cells designed for high temperature oil drilling applications.
(NASA Glenn Research Center, 2016)

## Slide 11: SCIENCE PAYLOAD
6.75 cm
5.00 cm
0.94 cm
0.76 cm
Chemical sensors
3-Axis Accelerometer (AD&C)
Micro Transmitter (Communications)
Low and High Temperature Batteries (Power)
PCB (C&DH)
Payload mass: 53 g

## Slide 12: MAXIMIZING FLIGHT TIME
THAT’S NOT FLYING
THAT’S FALLING… WITH STYLE
Planar “leaf” shape
Ballute / parachute
Inverted pyramid / shuttlecock
Long flight
Unstable
Faster descent
Mass approaches balloon
Self stabilizing
Intermediate flight time
© Disney Pixar

## Slide 13: PLATFORM
Fixed Rod
Moveable Rod
1.5 m
Thin film sheet
Support rods
Flat stowed configuration

## Slide 14: PLATFORM
Features
120 g total mass
  (~40% payload to structure ratio)
Collapses for flat packed stowage
Structure-as-science
  Inverted pyramid is a 10 GHz retroreflector

## Slide 15: HITCHING A RIDE TO VENUS
“mailbox” attached to carrier orbiter spacecraft (e.g. VERITAS / VOX)
Side by side stacks (50 each) 1.5 m x 1.5 m x 0.5m

## Slide 16: DEPLOYMENT
Where’s the aeroshell???
LEAVES has a ballistic coefficient of 0.173.
At the right altitude, and the right velocity, these probes can be deployed directly from orbit.

## Slide 17: DEPLOYMENT
Periapsis deployment during primary spacecraft aerobraking at 5 km/s
  Hp < 120 km results in nearly immediate entry (probable failure)
  120 < Hp < 145 km entry times between days and months (success)
  Hp > 145 km results in slow decay and no entry (probable failure)

## Slide 18: DATA GATHERING
30 km 224° C 9.3 hours

## Slide 19: DATA GATHERING
9.3 hours
~ 1600 km lateral drift
TIME (s)
Drift distance
Wind speed

## Slide 20: TRADE STUDIES
Drift distance
Wind speed
Areal Density | Time to Surface | Time to 35 km Altitude | Drift Distance | Maximum Heat Load | Maximum Force Loading
0.032 (kg/m2) | 4347 Min | 891.0 Min | 6056 km | 1.25 W/cm2 | 3.9 N/m2
0.063 (kg/m2) | 3130 Min | 627.0 Min | 4300 km | 2.54 W/cm2 | 7.7 N/m2
0.126 (kg/m2) | 2203 Min | 436.8 Min | 3014 km | 5.20 W/cm2 | 15.7 N/m2
0.253 (kg/m2) | 1533 Min | 300.1 Min | 2103 km | 10.70 W/cm2 | 32.5 N/m2

## Slide 21: COMMUNICATIONS AND POWER
Transmission triggered by radar signal
  400 MHz CDMA at ~ 3.5 kbps at 6000 km distance
LEAVES cache and transmit data from the start of record each time.
  Continuous acquisition of science data at 8 bps, navigation data at 80 bps.
  All gathered data transmitted in < 1 min.
Power use in data gathering mode: 0.15 W
Power use while transmitting: 1.5 W

## Slide 22: DATA GATHERING
(Orbiter 300 x 3000 km, 88.5°, T= 124 min)

## Slide 23: TECHNOLOGY INSPIRED BY FICTION
© Warner Bros, 1996
NOAA Totable Tornado Observatory (TOTO) extreme weather instrument (1984)
(which was inspired by reality)

## Slide 24: SUMMARY
DESTINATION: VENUS
UNIT MASS: 120 g
AREA: 1 m2
TOTAL UNITS: 100
LIFETIME: 9+ hours
FLIGHT READINESS: 3-5 YEARS
We gratefully acknowledge support by: